## Slide 1: Toward Spoofing-Resilient and Communication-Integrated MmWave Radar Sensing(SCR)
Vedran BEGanovic
MCS Project

## Slide 2: Spoofing Problem & SCR Concept
Spoofers can manipulate backscattered radar signals → generating “ghost targets”
GNSS spoofing (e.g., GPS L1/L5) demonstrates feasibility of signal deception
Automotive radar will need multi-frequency spoofing defenses
Spoofing-resilient and Communication-integrated Radar sensing scheme
SCR Methodology
Chirp-splitting - divides the chirp into sub-bands to detect suspicious Doppler peaks
Frame-splitting - separates uniformly vs. nonuniformly sampled chirps; spoof targets appear in uniform samples

## Slide 3: Evaluation Plan
MATLAB
  Signal Processing Toolbox
  Radar Toolbox
  Phased Array Toolbox
  No datasets or hardware experiments in this current project
  Metrics
    Peak Shift
    Peak magnitude difference

## Slide 4: FMCW Radar
Example – Object at rest
  Radar Parameters
    Carrier Frequency:
    Bandwidth:
    Sweep Time per Chirp:
    Sample Rate:
    # chirps per frame:
  Location: 18m from the radar
Figure 1: Peak location displays distance from radar

## Slide 5: Stationary vs Nonstationary (Doppler)
Example
  Object at rest
    Radar Parameters (as before)
    Location: 18m from the radar
  Object Moving
    Red line:
      Target Moving at
  Dashed vertical line
    Detected Doppler peak from the FT output
  Simulation matches theory
Doppler | Theoretical value [Hz] | Simulated Value [Hz] | Error [%]
Doppler | Theoretical value [Hz] | Simulated Value [Hz] | Error [%]
Figure 2: Stationary (left) and Nonstationary (right)

## Slide 6: SCR Spoofing
SCR performs two spoofing tests:
  Chirp-splitting → Velocity-modulation detection
  Each chirp split into two pieces:
    Lower half of chirp: slightly lower carrier frequency
    Upper half of chirp: slightly higher carrier frequency
  For a real/natural object → Doppler scales with the carrier frequency so the peaks line up
  For a modulated backscatterer / spoofer → Doppler independent of the carrier, so the peaks will misalign.
  Metric: Peak-Shift
    Doppler peak misalignment → Large shifts are more indicative of spoofing
SCR performs two spoofing tests:
  Frame-splitting → Distance-modulation detection
  Chirps grouped into two categories:
    Even-numbered chirps: uniform timing:
    Odd-numbered chirps: jittered timing:
  For a real/natural object → Do not depend on chirp timing, so peaks remain similar
  For a modulated backscatterer / spoofer → Relies on aliasing and collapses when timing is changed
  Metric: Peak magnitude difference
    Difference between coherent peak energy under uniform vs jittered → Large reductions is more indicative of spoofing
Notes: Uniform sampling → chirps occur at perfectly regular intervals
𝑡_𝑘=𝑘𝑇
Jittered sampling → chirps occur at irregular intervals
𝑡_𝑘=𝑘𝑇+𝛿_𝑘
where
𝛿_𝑘∼"small random jitter"
This jitter changes when the echo from each chirp is recorded.
spoofing reflectors (modulated retro-reflectors, RIS-based reflectors, or active repeaters):
Rely on sampling aliasing and phase alignment across chirps
Expect a uniform slow-time grid to produce constructive interference
Need that uniform grid to make their “fake” range bin appear
By breaking the uniformity, the radar interrupts the coherence that spoofing devices depend on.
Like clapping hands with someone, same rhythm is loud vs adding claps together random produces a weak clap
Coherent sum under uniform sampling
Under uniform chirp timing:
𝑡_𝑘=𝑘𝑇
A natural radar echo from a real object looks like:
𝑠(𝑘)=𝐴𝑒^(𝑗2𝜋𝑓_𝐷 𝑘𝑇)
Do Doppler FFT
produces a sharp, strong peak — called coherent peak energy.
Why?
Because the phase between chirps is predictable and consistent:
Δ𝜙=2𝜋𝑓_𝐷 𝑇 "(constant)"
All samples line up → constructive interference → strong peak.
Under jitter:
𝑡_𝑘=𝑘𝑇+𝛿_𝑘
Now:
𝑠(𝑘)=𝐴𝑒^(𝑗2𝜋𝑓_𝐷 (𝑘𝑇+𝛿_𝑘 ) )
The extra term:
𝑒^(𝑗2𝜋𝑓_𝐷 𝛿_𝑘 )
introduces random phase noise per chirp.
Phases no longer align
Doppler sinusoid becomes distorted
Energy spreads across many Doppler bins
Peak collapses
In other words:
Outcome: Coherence is destroyed
The FFT peak becomes smaller or disappears entirely.
Spoofing relies on signal aliasing, consistent sampling, to generate an artificial coherence → jitter destroys artificial coherence
SCR computes:
"PeakMagnitudeDiff"=(∣𝑃_"uniform" −𝑃_"jittered" ∣)/𝑃_"uniform"
Where:
𝑃_"uniform" = peak energy under uniform sampling
𝑃_"jittered" = peak energy under jittered sampling
Interpretation:
Real object:
𝑃_"uniform" ≈𝑃_"jittered" ⇒"small difference"
Spoofing reflector:
𝑃_"uniform" ≫𝑃_"jittered" ⇒"large difference"

## Slide 7: Chirp-Splitting
Natural Target at 18m moving at 1.2 m/s
Radar – 77GHz
Spoofing
  1 kHz spoofing reflector
  60% amplitude of the natural target
Figure 3: No spoofer – chirp peaks line up
Figure 4: Spoofer – chirp peaks exhibit splitting

## Slide 8: Frame-Splitting
Natural Target at 18m moving at 1.2 m/s
Radar – 77GHz
Spoofing
  1 kHz spoofing reflector
  60% amplitude of the natural target
Figure 5: No spoofer – chirp peaks line up
Figure 6: Spoofer – frame exhibits splitting

## Slide 9: References
K. Qian and P. Pathak, “Toward Spoofing-Resilient and Communication-Integrated MmWave Radar Sensing,” 2025.
M. L. Psiaki and T. E. Humphreys, “GNSS spoofing and detection,” Proceedings of the IEEE, vol. 104, no. 6, pp. 1258–1270, 2016.
D. Hunt, K. Angell, Z. Qi, T. Chen, and M. Pajic, “MadRadar: A Black-Box Physical Layer Attack Framework on mmWave Automotive FMCW Radars,” in Proceedings 2024 Network and Distributed System Security Symposium, San Diego, CA, USA: Internet Society, 2024. doi: 10.14722/ndss.2024.24153.
R. Reddy Vennam et al., “mmSpoof: Resilient Spoofing of Automotive Millimeter-wave Radars using Reflect Array,” in 2023 IEEE Symposium on Security and Privacy (SP), San Francisco, CA, USA: IEEE, May 2023, pp. 1807–1821. doi: 10.1109/SP46215.2023.10179371.

## Slide 10: Thank You! Questions/Comments